## Slide 1: CPE 301 Project Presentation Air Particulate Sensor POD v2
Jason Sikorski
sikorsk4@unlv.nevada.edu

## Slide 2: AIM & ACCOMPLISHMENTS
AIM:
Create a sensor package that can be used to monitor air quality
Store sensor data directly on SD card
Store sensor data remotely on an IoT cloud server
Display data using a web app interface
ACCOMPLISHMENTS
Sensor package was developed using 4 gas sensors, temperature sensor, GPS module, radio transmitter and SD card reader.
Modules were interfaced using ADC, SPI and UART interfaces.
Cloud storage was implemented using IBM Watson servers
Web App Interface was implemented using Intel Edison

## Slide 3: SCHEMATICS

## Slide 4: PCB Layout

## Slide 5: FINAL PCB

## Slide 6: DESIGN STAGES
Components
  AVR ATmega2560 - Microcontroller unit (MCU)
  MQ 2 - Analog Propane gas sensor
  MQ 5 - Analog Methane gas sensor
  MQ 7 - Analog Carbon Monoxide gas sensor
  MQ 136 - Analog Hydrogen Sulfide gas sensor
  TMP 136 - Analog Temperature sensor
  MTK3339 GPS Module
  Dylos DC1700 Air Particulate sensor
  SD Card
  XBee S3B 900MHz radio transmitter
  Intel Edison

## Slide 7: DESIGN STAGES
Interfaces
  ATmega2560 — MQ 2, MQ 5, MQ 7, MQ 136, TMP 136 — Analog to Digital Converter (ADC)
  ATmega2560 — MTK3339, DC1700, XBee S3B — Universal Asynchronous Receiver/Transmitter (UART)
  ATmega2560 — SD Card — Serial Peripheral Interface (SPI)
  XBee S3B — Intel Edison — Universal Asynchronous Receiver/Transmitter (UART)
Web Hosting
  Web App hosted by Intel Edison written in JavaScript
  MQTT transmission of data using JSON package to IBM Watson cloud written in JavaScript

## Slide 8: CODE DEVELOPMENT
Initialization
Initialize USART 0, 1, 2, 3
Set Timer 1 for 1 sec duty cycle
Mount SD Card/Open Write File
Enable Interrupts
Data Collection
Parse Dylos line
Parse GPS line
Call functions to read analog sensors
Construct String for SD card & radio transmit
Write to SD card
Send Data to XBee radio transmitter
Visualization
  Website hosted by Intel Edison
  IBM Watson cloud storage

## Slide 9: data interpretation
Dylos dc 1700
Transmit string format:
        15, 67
MTK3339 GPS Module
Transmit string format:
    $GPRMC,123519,A,4807.038,N,01131.000,E,022.4,084.4,230394,003.1,W*6A
    $GPGGA,123519,4807.038,N,01131.000,E,1,08,0.9,545.4,M,46.9,M,,*47
MQ Gas sensors
  Logarithmic chart: Resistance vs ppm
    Solve for resistance using a voltage divider circuit with calculated ADC voltage and known load resistance.
    Solve logarithmic function — RS = k ppmm
    Look up resistance value in a look up table.
Temperature sensor
  ADC conversion — ℃ = x mv - 50

## Slide 10: Video demonstration
Demo Link